## Slide 1: Parking Garage Slides for Sika Presentation
Parking Garage Maintenance Playbook
Western & Sika

## Slide 2: Conditions to be Checked
Part one
Parking Garage Maintenance Playbook

## Slide 3: Cracking
Noticeable fissures caused by construction or service-related stress resulting in moisture and chloride entry into the concrete.
Parking Garage Maintenance Playbook

## Slide 4: Scaling
The loss of the surface of the concrete caused by the freeze-thaw cycle and inadequate air entrainment in the concrete.
Parking Garage Maintenance Playbook

## Slide 5: Spalling
Potholes resulting from corrosion induced stress.
Parking Garage Maintenance Playbook

## Slide 6: Leaking
Tell-tale signs include standing water, stains, and possible damage to the floor below.
Parking Garage Maintenance Playbook

## Slide 7: Leaching
Water migration through the concrete slab that can result in corrosion of reinforcing steel and subsequent delamination and spalling of concrete.
Parking Garage Maintenance Playbook

## Slide 8: Exposed Reinforcing Steel
Caused by concrete deterioration resulting in dangerous corrosion of the reinforcing steel.
Parking Garage Maintenance Playbook

## Slide 9: Rust
Orange and brown staining that indicates corrosion.
Parking Garage Maintenance Playbook

## Slide 10: Parts of the Garage to Inspect
Part two
Parking Garage Maintenance Playbook

## Slide 11: Concrete Beams
A visual survey should be done to detect corrosion and exposed steel.
Parking Garage Maintenance Playbook

## Slide 12: Concrete Slabs
Floors and ceiling should be carefully checked for normal wear, initial and advanced deterioration.
Parking Garage Maintenance Playbook

## Slide 13: Drains
Check for obstruction causing water to pond and possibly leach through the concrete slabs.
Parking Garage Maintenance Playbook

## Slide 14: Walls
Check for cracks, water entry points, and other signs of stress and deterioration.
Parking Garage Maintenance Playbook

## Slide 15: Expansion and Control Joints
Check for joint failure or damage from traffic or snow plows.
Parking Garage Maintenance Playbook

## Slide 16: Support Columns
Monitor for any signs of cracking or stress.
Parking Garage Maintenance Playbook