## Slide 1
Ensuring longevity and safety through regular upkeep
Notes: AI-generated content may be incorrect. ---

## Slide 2: Who is western specialty contractors?

## Slide 3: America’s largest building envelope restoration contractor
Founded in 1915
30+ Branches Nationwide
Family Owned & Operated for 115 years
Employee owned since 2026
Invested in Client Satisfaction
Clients Are Our Partners
95% of Services are Self-Performed
Industry Leader in Safety
Notes: Western Specialty Contractors serves as a trusted preferred vendor through Deltaworks, providing specialized expertise when conditions exceed routine maintenance or present an immediate safety concern. Facility teams should contact Western when they encounter deepening or rapidly spreading cracks, persistent leaks that continue despite drain cleaning, or visible rebar exposure, as these signs indicate that deterioration is beyond surface-level repair. Hollow‑sounding slabs, widespread spalling, or any structural distress in beams or columns also require professional evaluation. Western brings advanced inspection techniques, corrosion mitigation strategies, and structural repair capabilities that adhere to best‑practice safety and industry standards. Additionally, Western’s familiarity with Delta and JLL expectations ensures streamlined communication, quicker mobilization, and coordinated project execution. Engaging Western early not only restores structural integrity but also prevents hazards from escalating, offering peace of mind to facility managers responsible for high-traffic environments such as airport parking structures or operational facilities.

## Slide 4
Western’s Core Services for Parking Decks and Buildings
Concrete, Facade and Masonry Restoration
Caulking/Sealing/Tuckpointing
Expansion Joint Systems
Exterior Wall Coatings
Parking & Plaza Deck Restoration
Roofing Repairs and Restoration
Waterproofing
Historic Restoration
Notes: Western Specialty Contractors offers a comprehensive range of services designed to enhance safety, durability, and performance across parking structures and building envelopes. Core capabilities include structural concrete repair such as spall patching, form‑and‑place repairs, and shotcrete applications. Western’s waterproofing expertise ensures effective protection against moisture infiltration through deck coatings, sealants, and joint replacement. Masonry restoration services address deterioration in brick, stone, and façade systems with techniques such as tuckpointing, repointing, and material replacement. For structural strengthening, Western provides reinforcement solutions that address corrosion‑related weakening or load‑capacity concerns. The company also performs detailed inspections, condition assessments, and leak investigations that support long-term asset management strategies. These services collectively contribute to safer environments, prolonged structural life, and reduced operational risks, making Western a valuable partner for Delta, JLL, and other facilities teams responsible for maintaining high-traffic environments.

## Slide 5: Importance of building envelope Preventive maintenance
Notes: Daily and Weekly Preventive Actions for Facility Teams, When to Engage Western as a Preferred Deltaworks Vendor

## Slide 6
Deferred Maintenance Escalation
Approximately 20% growth of repair area annually
Approximately 3-5% cost increase annually

## Slide 7: Proper Budgeting and Proactive Maintenance
Reduces Overall Repair Cost
Addressing minor issues early prevents them from becoming major, high-cost repairs.
Extends Asset Life
Protects façades, roofing systems, parking structures, waterproofing systems, and building components from accelerated deterioration.
Minimizes Emergency Repairs
Planned maintenance reduces unexpected failures that disrupt operations and strain budgets.
Improves Safety
Identifies hazards such as spalling concrete, trip hazards, water intrusion, and deteriorated building components before they create risks for occupants and visitors.
Supports Operational Continuity
Helps avoid facility shutdowns, tenant disruptions, and business interruptions caused by unexpected failures.
Extends Asset Life
Protects façades, roofing systems, parking structures, waterproofing systems, and building components from accelerated deterioration.
Protects Property Value
Proactively correcting deficiencies helps limit potential claims related to injuries, falling debris, water damage, or structural issues.
Improves Tenant Satisfaction
Fewer disruptions, leaks, closures, and safety concerns create a better experience for building users.
Notes: Facility teams play a central role in maintaining safety and reliability in parking structures and building envelopes. Daily and weekly walkthroughs allow personnel to identify early signs of deterioration before they escalate into hazardous conditions. Key tasks include monitoring drive lanes and walkways for cracks, spalls, potholes, and changes in surface texture that might indicate subsurface issues. Teams should inspect drains regularly to ensure they are free from debris, as poor drainage is a leading cause of corrosion and slipping hazards. Seasonal considerations—such as freeze–thaw cycles—require increased vigilance, as water infiltration during colder months can accelerate deterioration. Facility staff should also examine expansion joints, sealants, and transitions for gaps or tearing that could allow water migration. Documenting observations with photographs and maintaining an ongoing log helps track the progression of conditions over time and supports more accurate assessments when external contractors are involved. Through consistent monitoring, early reporting, and understanding basic deterioration patterns, facility teams can significantly reduce the likelihood of structural hazards, improve safety, and minimize unexpected operational disruptions.

## Slide 8: FaCade Preventive Maintenance and Budgeting
Notes: Importance of Preventive Maintenance for Facility Safety

## Slide 9: Types of Commercial Building Construction

## Slide 10: Mass Masonry

## Slide 11
Veneer Wall System

## Slide 12: Curtain Wall

## Slide 13
Precast Concrete

## Slide 14: Terra Cotta

## Slide 15: Facade Repair Timeline
15-20 Years
Silicone sealant replacement
20-25 Years
Tuckpointing
Masonry restoration
Structural – steel and pinning
Replicas – FRP & GFRC
5-10 Years
Building cleaning and sealing
Support steel replacement
Lintels and shelf angles
Flashing
Urethane sealant replacement
Wet Seal/wet glaze

## Slide 16: Stucco

## Slide 17: EIFS

## Slide 18: Stucco & EIFS Repair Timeline
5-10 Years
Urethane sealant replacement
10-15 Years
Failed corner bead
Crack/spall repair
Lathe replacement/patching
Vapor barrier
Flashings
Repair of insulating material and mesh
Finish Coat Replacement and Patching
Punctured and damaged EIFS
Wall coatings

## Slide 19: In-House Inspections
Efflorescence
Window Leaks
Sealant Failures
Window Lintels, Sills, & Mullions
Cracking / Rust / Delamination
Delaminated Coating

## Slide 20: In-House Inspections
Parapet Wall & Caps
Window Gaskets / Sealant
Roof Flashing
Cracking
EIFS / Stucco Delamination

## Slide 21: In-House Inspections
Deteriorated Mortar Joints
Environmental Containments / Build-Up

## Slide 22: Parking garage Preventive Maintenance and Budgeting
Notes: Importance of Preventive Maintenance for Facility Safety

## Slide 23
COMMON TYPES OF PARKING STRUCTURES

## Slide 24
POST TENSION

## Slide 25
PRE-CAST

## Slide 26
PRE-CAST

## Slide 27
CAST IN PLACE

## Slide 28: In-House Inspections Where to Look
Concrete Beams
Concrete Slabs
Walls
Drains
Support Beams

## Slide 29: In-House Inspections
Corrosion
Cracking
Delamination

## Slide 30: In-House Inspections
Scaling
Leaching
Deck Coat Peeling

## Slide 31: In-House Inspections
Expansion Joint
Deteriorated Sealant
Exposed Structural Steel

## Slide 32
Cracks allow for water to penetrate to the structural steel
Structural steel begins to corrode
Corrosion causes steel to expand
Concrete begins to delaminate and spall
Steel will continue to corrode, causing loss of strength in structural steel
Before Corrosion.
What is happening underneath the surface
Further corrosion. Surface cracks. Stains.
Build-up of corrosion products.
Eventual Spalling. Corroded Bar. Exposed.

## Slide 33: Protecting your investment
Notes: Cracking, Scaling, and Spalling Risks, Leaking, Drainage Failures, and Water Intrusion, Corrosion, Rust, and Exposure of Reinforcing Steel, Key Structural Components to Inspect Regularly

## Slide 34
Why
To Protect Concrete, Particularly After Repairs
Application
New Concrete Areas
Repair and Maintenance of Existing Coatings
Deck Coating

## Slide 35
BEFORE
AFTER

## Slide 36
Annually
Maintenance Items:
5-10 Years
Deck Coatings
15-20 Years
Continued concrete maintenance
Delaminated, cracking, and/or falling concrete
Immediate Safety Concerns
Stall striping visibility
Sealants
Concrete cracking maintenance
Maintaining striping/signage is withing ADA compliance
Preventive maintenance: add sealers or protective coatings
Exposed structural steel components
GARAGE REPAIR TIMELINE

## Slide 37: Roofing Preventive Maintenance and Budgeting
Notes: Daily and Weekly Preventive Actions for Facility Teams, When to Engage Western as a Preferred Deltaworks Vendor

## Slide 38
SINGLE-PLY:
Single-ply roofing can be applied to multiple types of system assemblies. Each type has unique benefits and options:
  TPO
  PVC
  EPDM
BUILT-UP ROOF (BUR) SYSTEM:
Multiple layers of asphalt get applied between ply sheets (or felts) over the roof deck and insulation.
MODIFIED BITUMEN:
Modified bitumen roofing systems are made by mixing asphalt with polymers and reinforcing it with fabric mats in the factory.
  APP
  SBS
GREEN ROOFING:
Applied over multiple types of approved roof assemblies, green roofs can help with stormwater management and sustainability.
LIQUID APPLIED:
Liquid-applied systems can be used to repair a damaged roof but also can be used to restore and increase the life span of an old roof.
COMMON TYPES OF ROOF SYSTEMS

## Slide 39
Single-Ply TPO & PVC
Single-Ply EPDM
Built-up Roof (BUR)
Modified Bitumen
Green Roof
Liquid Applied
ROOFING SYSTEMS

## Slide 40
Wall Flashing
Roof Drain / Debris
Roof Penetrations
Roof Covering Condition
Evidence of standing water or “ponding”
Scupper
Equipment Curbs
Skylights
Roof Slope
Metal Flashing
ROOFING TERMS

## Slide 41: COMMON ROOF FAILURES
Ponding Water
Seam Failures
Blistering
Improper Repairs
Tenting
Roof Debris

## Slide 42: Common Roof Failures
Blistering
Ridges and Wrinkles
Alligatoring

## Slide 43: Common Roof Failures
Contamination
Failed Flashing
Failed Coatings

## Slide 44
Typical Life Cycle = 20 Years
0-3 YEARS The Honeymoon
Annual inspections help identify and correct minor issues before they become costly repairs
Protect warranty coverage by addressing damage from weather, foot traffic, and maintenance activities early
3-5 YEARS Set Good Habits
Establish a proactive inspection and maintenance program to maximize roof life
Regularly evaluate flashings, penetrations, and sealants to prevent future leaks and water intrusion.
5-15 YEARS Preventive Maintenance & Repairs
Routine maintenance and timely repairs significantly extend service life and reduce lifecycle costs
Inspect after major weather events and keep drains and drainage systems clear to prevent water damage
15-20 YEARS Re-Roofing or Restoration Planning
Begin evaluating restoration and replacement options before roof conditions become critical
Develop a long-term capital budget and asset plan to avoid unexpected expenditures

## Slide 45
Annually
Internal roof inspection after weather event (debris and damage)
5-10 Years
Preventive maintenance
15-20 Years
Restoration extending useful life
Inspection completed by third party for maintenance items
Caulking, pitch pockets, ponding, vegetation growth, etc
Overlay
Replacement
ROOF REPAIR TIMELINE

## Slide 46
  All systems are monolithic and can be locally or fully reinforced.
  Liquid membranes conform to complicated details and penetrations with ease and little to no waste.
  Increases useful life of existing roof
  Cost efficient
  Eco-friendly
  Additional insulation not required
  Is not considered a roof layer
Roof Restoration Liquid Applied

## Slide 47: Choosing the right contractor and material
Notes: Daily and Weekly Preventive Actions for Facility Teams, When to Engage Western as a Preferred Deltaworks Vendor

## Slide 48: Importance of utilizing proper material
Maximizes Service Life
Materials selected for the specific environment and exposure conditions last longer and perform better over time.
Reduces lifecycle costs
The right material minimizes premature failures, maintenance expenses, and future replacement costs.
Supports warranty and system compatibility
Using compatible products within a complete system helps ensure manufacturer warranties remain valid.
Protects owner’s investment
Quality materials preserve asset value and help avoid costly emergency repairs.
Material Options
When working with an engineer or consultant, encourage them to specify multiple approved material manufacturers and products rather than a single product
  Encourages competitive pricing
  Provides flexibility for material availability and lead times
  Allows contractor to recommend the best fit
Notes: Facility teams play a central role in maintaining safety and reliability in parking structures and building envelopes. Daily and weekly walkthroughs allow personnel to identify early signs of deterioration before they escalate into hazardous conditions. Key tasks include monitoring drive lanes and walkways for cracks, spalls, potholes, and changes in surface texture that might indicate subsurface issues. Teams should inspect drains regularly to ensure they are free from debris, as poor drainage is a leading cause of corrosion and slipping hazards. Seasonal considerations—such as freeze–thaw cycles—require increased vigilance, as water infiltration during colder months can accelerate deterioration. Facility staff should also examine expansion joints, sealants, and transitions for gaps or tearing that could allow water migration. Documenting observations with photographs and maintaining an ongoing log helps track the progression of conditions over time and supports more accurate assessments when external contractors are involved. Through consistent monitoring, early reporting, and understanding basic deterioration patterns, facility teams can significantly reduce the likelihood of structural hazards, improve safety, and minimize unexpected operational disruptions.

## Slide 49
Protects your investment
The right contractor focuses on long-term building performance, not just completing the immediate repair. Proper repairs help maximize the useful life of building assets.
Reduces total cost of ownership
Quality workmanship and appropriate repair methods minimize recurring issues, repeat repairs, and costly callbacks.
Partners in asset management
The best contractors act as trusted advisors, providing assessments, maintenance recommendations, repair prioritization, and lifecycle planning.
Provides reliable warranties and accountability
Reputable contractors stand behind their work and provide meaningful warranty support when issues arise
Minimizes disruption to tenants
Experienced contractors can plan repairs strategically to reduce downtime, tenant inconvenience, and interruptions to daily business operations.
Delivers appropriate repair solution
Not all repairs are equal. Experienced contractors understand building systems and recommend solutions that address root causes, not just symptoms.
Provides accurate scope and pricing
The right contractor helps ensure repairs are properly quantified, specified, and priced, allowing facility managers to make informed decisions when comparing proposals.
Notes: Facility teams play a central role in maintaining safety and reliability in parking structures and building envelopes. Daily and weekly walkthroughs allow personnel to identify early signs of deterioration before they escalate into hazardous conditions. Key tasks include monitoring drive lanes and walkways for cracks, spalls, potholes, and changes in surface texture that might indicate subsurface issues. Teams should inspect drains regularly to ensure they are free from debris, as poor drainage is a leading cause of corrosion and slipping hazards. Seasonal considerations—such as freeze–thaw cycles—require increased vigilance, as water infiltration during colder months can accelerate deterioration. Facility staff should also examine expansion joints, sealants, and transitions for gaps or tearing that could allow water migration. Documenting observations with photographs and maintaining an ongoing log helps track the progression of conditions over time and supports more accurate assessments when external contractors are involved. Through consistent monitoring, early reporting, and understanding basic deterioration patterns, facility teams can significantly reduce the likelihood of structural hazards, improve safety, and minimize unexpected operational disruptions.

## Slide 50
Dissection of a Proposal
The same scope of work
Approved material
Warranty (contractor standing behind their work)
Quantity of repair (quantified as linear feet, cubic feet, or square feet)
Verbiage on material utilization

## Slide 51
High Risk Proposal

## Slide 52
Strong Proposal

## Slide 53: Conclusion
Notes: Key Takeaways and Commitment to Safety

## Slide 54
Budgeting
Components
Get to know the components that make up the building envelope
Understand
Understand age and remaining useful life of components
Work
Work with contractors / consultant / engineer to identify issues early
Inquire
Inquire about phasing options to minimize financial impact
Advantage
Advantage in allowing contractors adequate time to prepare scopes and pricing

## Slide 55: Key Takeaways
Importance of Preventive Maintenance and Budgeting
  Preventive maintenance protects the structural integrity and operational safety of the building envelope.
Early Detection Benefits
  Early detection of damage reduces risks, prevents accidents, and extends the lifespan of infrastructure.
Choosing the Right Material and Contractor
  Choosing the right material and contractor for your project is critical to ensuring repairs are completed safely, correctly, and cost-effectively, helping building owners maximize asset life and minimize future maintenance and repair expenses.
Notes: Preventive maintenance is essential for protecting the structural integrity and operational safety of parking decks and facilities. Early detection of cracking, spalling, corrosion, and drainage failures significantly reduces risks, prevents accidents, and extends the lifespan of critical infrastructure. Facility teams play a key role in identifying early warning signs, while Western Specialty Contractors provides the advanced expertise needed when deterioration reaches more serious levels. As a preferred vendor through Deltaworks, Western is committed to supporting Delta and JLL with industry‑leading safety practices, superior repair capabilities, and reliable long-term solutions. Together, proactive inspection and professional intervention create a safer, more predictable environment for employees, tenants, and the public.

## Slide 56: Western has your back!
Masonry Restoration
  Tuckpointing, repointing, and material replacement restore brick, stone, and façade systems effectively.
Structural Concrete Repair
  Services include spall patching, form-and-place repairs, and shotcrete to restore concrete integrity.
Waterproofing Solutions
  Deck coatings, sealants, and joint replacements prevent moisture infiltration and protect structures.
Roofing
  Leak investigation and repairs, restoration, overlays, replacement, and new construction installation.

## Slide 57
ASSISTANCE WITH ASSET MANAGEMENT, BUDGET PLANNING, PROJECT PHASING
INDUSTRY EXPERTS PART OF YOUR MANAGEMENT TEAM
TRAINING & EDUCATION:
MAINTENANCE PROGRAM, REPAIR PRIORITIZATION
NATIONAL FOOTPRINT
CONSISTENCY = QUALITY CONTROL PROGRAM
TOP RATED SAFETY PROGRAM
OSHA = 1.82
EMR = 0.69

## Slide 59: We want to help!! Reach out today
Daniele Portal
Steven Johnson
Chester Scott
Business Development Manager
305-812-6498
DanieleP@Westerngroup.com
Sr. Sales/Project Manager
404-398-9432
StevenJ@Westerngroup.com
Sr. Sales/Project Manager
404-435-0763
ChesterS@Westerngroup.com